## Slide 1: Grid Enhancing Technologies Julia Selker, Executive Director, WATT Coalition October 2024

## Slide 2: Agenda
About the WATT Coalition
Order 1920 on Transmission Technologies
What are GETs
Benefits of GETs
Barriers
Policy

## Slide 3: Grid Enhancing Technologies: hardware, software, or both that dynamically increase the capacity, efficiency, reliability or safety of power lines, faster and at lower cost than traditional grid infrastructure.
Mission statement:
The Working for Advanced Transmission Technologies (WATT) Coalition advocates for policy that supports wide deployment of Grid Enhancing Technologies (GETs) to accelerate the clean energy transition and lower energy costs.
www.watt-transmission.org

## Slide 4: Order No. 1920 on Transmission Technologies (see pages 845-848)
Require transmission providers in each transmission planning region to consider
  dynamic line ratings
  advanced power flow control devices
  advanced conductors
  and transmission switching
  for each identified transmission need, in long-term regional planning and Order 1000 processes.

## Slide 5: More from Order No. 1920
For new facilities and upgrades
Evaluate whether ATTs alone or with other upgrades “would be more efficient or cost-effective than selecting new regional transmission facilities or upgrades to existing transmission facilities that do not incorporate these technologies.”
Evaluate against all required benefits and standard selection criteria, and follow Good Utility Practice

## Slide 6: What are Grid Enhancing Technologies?
Dynamic Line Ratings
Dynamic Line Ratings (DLRs) measure and calculate the true carrying capacity of transmission lines – often finding 20% or more capacity than assumed.
Topology Optimization
Topology Optimization is software that finds the best use of grid infrastructure to redistribute power and unlock more capacity.
Advanced Power Flow Control
Advanced Power Flow Control redirects power to lines with extra capacity, preventing overloads and balancing the use of the grid.

## Slide 7: Why do we need GETs ASAP?

## Slide 8: Benefits of Grid Enhancing Technologies (GETs)
Cost Savings
  Decrease congestion/redispatch costs by ~40%
  Resolve constraints for 1/20-1/200th the cost of traditional upgrades
  Increase transmission capacity by 20%+ over 90% of the time
  Enable cheaper generation/load interconnection
Faster grid capacity for load and generation
  Brattle study showed GETs could double capacity for new generation, without new lines
  GETs deploy in months
Reliability through flexibility and awareness
  Data-driven decisions, real-time visibility, and enhanced control over the system support reliable grid operation
  Extreme weather can put system at risk without monitoring and control
  DLR devices can monitor for wildfire risk

## Slide 9: Growing generator interconnection queues
Congestion

## Slide 10: Today’s grid is inefficient because it is underutilized. An interconnection study showed a 3% line overload in high wind scenarios, requiring a $50 million rebuild – DLR was not considered.
Large load!?

## Slide 11
NewGrid presentation to FERC
Reduce grid congestion by 40%
Saving billions!
2x clean energy interconnection
Notes: Grid congestion isn’t the only value of GETs – we need to access the latent capacity on the grid so that we plan correctly, so that we interconnect the cheapest, cleanest resources, and enable new industry.

## Slide 12
Benefits:
GETs deploy in months
For cheap!
1/20-1/200th the cost
NEMA 2024, continues for 2 more pages

## Slide 13
Benefits of GETs:
Monitoring and control supp0rt resilience and reliability.

## Slide 14: Transmission expansion paves the road to the future
“To unlock the full emissions reduction potential of the Inflation Reduction Act,
the pace of transmission expansion must more than double
the rate over the last decade”
https://repeatproject.org/docs/REPEAT_IRA_Transmission_2022-09-21.pdf

## Slide 15: Adoption in the US – many pilots, few in operations
PPL Electric Utilities: First operational DLR deployment reduced congestion by $60 million in first year, expecting $23 million per year ongoing

## Slide 16: Barriers for GETs: Institutional Inertia + Incentives
Regulator support for innovation
  Innovation for customer benefit should be encouraged
Prioritization of system and process changes
  Many planners, utility executives, and stakeholders have never evaluated or deployed advanced transmission technologies
Incentives
  Lower returns on lower capital cost expenditures, and uncertainty about cost recovery

## Slide 17: Policy for GETs

## Slide 18: State regulation and legislation
PUCs ask how GETs are being evaluated
  Colorado PUC Transmission Planning Docket (Proceeding 23M-0472E)
Require GETs/HPC evaluation in CPCN applications
  Original VA legislation (HB862)
  Loading order policy: optimization first, then reinforcement, then expansion
Create incentives for utilities to go after federal funding for GETs/HPC deployment.
  Washington UTC ROE adder on federal $ (Docket U-240013)
Require GETs/HPCs in economic and reliability transmission planning or commissioning studies.
  Minnesota law
  California law
  Illinois Commerce Commission Renewable Energy Access Plan (22-0749)
  New York Coordinated Grid Planning Process/ATWG (Case 20-E-0197)

## Slide 19: Federal policy
White House + 22 governors share goal to upgrade 100k miles of grid in 5 years – Nevada could join!
DOE – billions in eligible IIJA programs will help build utility experience with GETs (and further grants through EPA, USDA)
  CA won $600 million federal grant for DLR and reconductoring.
FERC Order No. 881 mandates that RTOs accept dynamic line ratings by 2025, and utilities use Ambient Adjusted Ratings.
FERC Order No. 2023 requires the consideration of Advanced Power Flow Control in generator interconnection processes, with Topology Optimization and Dynamic Line Ratings as optional.
FERC Order No. 1920 requires GETs in Order 1000 planning and 20-year planning, to replace or improve other upgrades.

## Slide 20: Pending federal action
FERC Docket No. RM24-6 is an Advanced Notice of Proposed Rulemaking to require solar heating to be included in line ratings, and DLR with wind-speed cooling on some transmission lines.
FERC is considering additional proposals to bring GETs into common practice
  Shared savings incentive (RM20-10 & AD19-19)
    Advancing GETs Act S. 3918 would require FERC to implement a shared savings incentive.
  Improved transmission operations oversight (AD22-8)

## Slide 21: Working for Advanced Transmission Technologies
For more information contact
Julia Selker / jselker@gridstrategiesllc.com
www.watt-transmission.org

## Slide 22: Appendices

## Slide 23: Dynamic Line Ratings
First movers:
Since 2012, Belgium sees >20% capacity increases >90% of the time (increase capped at 30%).
PPL Electric Utilities reduces redispatch costs by $60 million in first year of 2-line DLR deployment
AES found 61% average capacity increase over static line ratings on a 345kV line
Notes: AAR incorporates hourly temperature, whether sun is up.

## Slide 24: Advanced Power Flow Control
VELCO DOE GRIP Grant with EPRI to increase VT-NY transfer capacity
Central Hudson unlocks 185 MW of transmission capacity
California utilities identify reliability applications

## Slide 25: Topology Optimization
ISO New England and SPP using Topology Optimization for outage planning
ERCOT and MISO allow reconfigurations for congestion mitigation
Study: Topology Optimization could reduce PJM congestion costs by 50% on average

## Slide 26: Considerations for GETs in transmission planning

## Slide 27: Advanced Power Flow Control
APFC can be modeled as adjustable reactance in steady-state transmission planning models, by adding a “Modular Static Synchronous Series Compensator.”
  In production cost modeling, a utility can model variable reactance.
  Modeling packages exist to automatically insert MSSSCs, or utilities can work with vendors for assessment.
  Modeling packages are available for dynamic studies.

## Slide 28: Dynamic Line Ratings
Scenarios should be self-consistent – if a line has 20%+ more capacity all winter, that should be recognized.
DLR can be deployed to mitigate constraints if they emerge before new infrastructure comes into service.
Many other study inputs are uncertain – planners can choose confidence levels when applying DLR uprates in planning scenarios.

## Slide 29: Topology Optimization
Generation retirements and additions and new transmission infrastructure change grid topology.
  Reconfigurations could resolve constraints that emerge with these changes at negligible cost.
Planners may find value in increasing optionality for future reconfigurations through substation design.

## Slide 30: Applications of GETs
Transmission and distribution planning
Outage planning and coordination
Contingency planning
Generation interconnection studies
Operations decision making
Non-wire alternatives evaluation
Sources available upon request
PowerFactory INTEGRAL Organon ASPEN MATLAB®/Simulink® PSCADTM/EMTDC | PSLF PSS®E RSCAD/RTDS TSAT PowerWorld NEPLAN
Advanced Power Flow Control models available:

## Slide 31: Other resources to check out

## Slide 32: Recommended reading
Time Series Power Flow and Contingency Analysis with Weather Adjusted Line Ratings: A Synthetic WECC Case Study by Hui Zhang, Natalie Diltz, Rajarshi Roychowdhury, Xuan Wu – AES Corporation

## Slide 33: DLR capacity increases can be surprising!
SUSQ-HARW DLR Simulation Data Vs Actual at Emergency Rating Temperature
(Winter Months)
Chart: Hour (December - April)

## Slide 34: Examples of Grid Enhancing Technologies in Planning
https://watt-transmission.org/wp-content/uploads/2023/04/Building-a-Better-Grid-How-Grid-Enhancing-Technologies-Complement-Transmission-Buildouts.pdf